## Slide 1: INDUSTRIAL PUMP SYSTEMS Custom Manufactured for Sutphen Corporation

## Slide 2: ‘
FOAM PROPORTIONING SYSTEMS
AccuMax: Flow Based Direct Discharge Injection
Hot Shot-II & Servo Command: Demand Balanced Pressure

## Slide 3: AccuMax Multi-Point, by FoamPro
Flow Based Direct Discharge Injection Foam Proportioning System
Master Control Digital Display
Digital Display Line Controller x # of Foam Capable Discharges
Flowmeter Line Controller x # of Foam Capable Discharges
Edwards Rotary Gear Foam Pump, 90, 150, & 300-GPM
NOTE: 90-GPM allows for Hydraulic Pump to be Fire Pump Transmission Auxiliary Drive-Driven

## Slide 4: HOT SHOT-II, by Williams Fire Control
Demand Type Balance Pressure Foam Proportioning System
System Control Panel
Rotary Foam Metering Valve x # of Foam Discharges
Ratio Controller (Venturi) x # of Foam Capable Discharges
Edwards Rotary Gear Foam Pump, 60, 150, 250 & 300-GPM

## Slide 5: Servo Command, by NATIONAL FOAM
Demand Type Balance Pressure Foam Proportioning System
System Main Control Panel
Rotary Foam Variable Proportioning Valve (VPV) x # of Foam Discharges
Foam Concentrate Proportioner (Venturi) x # of Foam Capable Discharges
Edwards Rotary Gear Foam Pump, 150, & 300-GPM

## Slide 6: INDUSTRIAL FIRE PUMP SYSTEMS HALE 8F 3000-GPM / WATEROUS CRU-2 4000-GPM

## Slide 7: INDUSTRIAL WATER PUMP SYSTEMS MIDSHIP or REAR MOUNT
MIDSHIP SPLIT-SHAFT PUMP SYSTEMS:
REAR MOUNT PUMP/MIDSHIP SPLIT-SHAFT SYSTEMS

## Slide 8: SPLIT-SHAFT WATER PUMP TRANSMISSIONS WATEROUS: CHAIN DRIVE – HALE & DARLEY: GEAR-DRIVE
  Waterous CRU-2C21 (TC21 Rear Mount): 16,000 ft. lb.
    C-21 CHAIN Drive Front Transmission/Suction Facing Rear (for Aerials)
    C-21 CHAIN Drive Rear Transmission/Suction Facing Front (for Pumpers)
  Hale 8FG or 8FK: “G” (RGA Rear Mount): 16,000 ft. lbs. “K” 18,500 ft. lbs.
    G or K, GEAR Drive Front Transmission/Suction Facing Rear (for Aerials)
    G or K, GEAR Drive Rear Transmission/Suction Facing Front (for Pumpers)
  Darley ZSM: MegaTrans (MegaTrans PTO Rear Mount): 19,300 ft. lbs.
    GEAR Drive Front Transmission/Suction Facing Rear (for Aerials)
    GEAR Drive Rear Transmission/Suction Facing Front (for Pumpers)

## Slide 9: WATER PUMPS BRAND/TYPE/MODEL/CAPACITIES WATEROUS SINGLE STAGE, SINGLE SUCTION IMPELLER, SPLIT-SHAFT DRIVEN

## Slide 10: WATER PUMPS BRAND/TYPE/MODEL/CAPACITIES HALE SINGLE STAGE, SINGLE SUCTION IMPELLER, SPLIT-SHAFT DRIVEN

## Slide 11: WATER PUMPS TYPE/BRAND/MODEL/CAPACITIES DARLEY SINGLE STAGE, SINGLE SUCTION IMPELLER, SPLIT-SHAFT DRIVEN

## Slide 12: NFPA 1901 PUMP SYSTEM & SUCTION CAPABILITIES 2016 EDITION: 3000-GPM & ABOVE@ 100 PSI

## Slide 13: NFPA 1901 PUMP SYSTEM & SUCTION CAPABILITIES 2009 EDITION: 3000-GPM AND BELOW@ 150 PSI

## Slide 14: INDUSTRIAL PUMP MODULE APPLICATIONS
INDUSTRIAL PUMPERS & PUMPER TENDERS/TANKERS
SAI: INDUSTRIAL AERIALS
SPI: INDUSTRIAL AERIAL PLATFORMS

## Slide 15: INDUSTRIAL PUMPER & PUMPER/TANKER PUMP MODULES
  Side Mount, Street Side Controls
    LDH (8” reduced to 6”) Suctions 2-Curb Side / 2-Street Side (Optional 5” Rear is Available) + Multiple 2-1/2”
    LDH (5” or 6”) Discharges Curb Side and Rear (None Street Side) + Multiple 2-1/2”
    Overhead 2” and/or 2-1/2” Cross-Lays
    Forward “Stacked” 2” and/or 2-1/2” Speed-Lays
    Overhead Monitors, 1000 to 5000-GPM Akron, 2000 to 6000-GPM Williams
    Rear Monitors, 1000 to 2000-GPM
  Top-Mount Controls “Open/Exposed” or “Fully Enclosed”
    LDH (8” reduced to 6”) Suctions 2-Curb Side / 2-Street Side (Optional 5” Rear is Available) + Multiple 2-1/2”
    LDH (5” or 6”) Discharge: Driver Side, Curb Side and Rear + Multiple 2-1/2”
    Overhead 2” and/or 2-1/2” Cross-Lays
    Forward “Stacked” 2” and/or 2-1/2” Speed-Lays
    Overhead Monitors, 1000 to 5000-GPM Akron, 2000 to 6000-GPM Williams
    Rear Monitors, 1000 to 2000-GPM
  Rear-Mount Controls
    LDH (8” reduced to 6”) Suctions Up To 3-Opposite Side of Operator’s Panel and/or Rear + Multiple 2-1/2”
    LDH (5” or 6”) Discharges: Opposite Side of Operator’s Panel and/or Rear + Multiple 2-1/2”
    Overhead Rear Monitor(s), 1000 to 5000-GPM Akron, 2000 to 6000-GPM Williams
    Midship Monitor(s), 1000 to 2000-GPM

## Slide 16: INDUSTRIAL PUMPER & PUMPER-TANKER SIDE MOUNT PUMP CONTROLS
AccuMax, Hot Shot-II or Servo Command
(Hot Shot-II System Shown)

## Slide 17: INDUSTRIAL PUMPER & PUMPER-TANKER TOP-MOUNT PUMP CONTROLS
AccuMax Hot Shot-II Servo Command

## Slide 18: TOP MOUNT PUMP CONTROLS Open Walkway < + > Fully Enclosed

## Slide 19: HIGH VOLUME MONITOR SUPPORT STRUCTURE 2:1 SAFETY FACTOR @ 6000-GPM

## Slide 20: INDUSTRIAL AERIAL & AERIAL PLATFORM PUMP MODULES
SAI-75 & 85+: Industrial Aerial, Side Mount, Street Side Controls
  LDH (8” reduced to 6”) Suctions 3-Curb Side (Optional 5” Rear is Available) + Multiple 2-1/2”
  LDH (5” or 6”) Discharges Curb Side Only + Multiple 2-1/2”
  Midship 2” and/or 2-1/2” Cross-Lays
  Midship Monitor(s) 1000 to 2000-GPM
  Aerial Waterway (8” reduced to 5” Swivel)
SPI: Industrial Platform, Side Mount, Street Side Controls
  LDH (8” reduced to 6”) Suctions 3-Curb Side (Optional 5” Rear is Available) + Multiple 2-1/2”
  LDH (5” or 6”) Discharges Curb Side Only + Multiple 2-1/2”
  Midship 2” and/or 2-1/2” Cross-Lays
  Midship Monitor(s) 1000 to 2000-GPM
  Aerial Waterway (8” reduced to 5” Swivel)

## Slide 21: INDUSTRIAL AERIAL & PLATFORM MODULES
SAI-75 Pump Module SAI-85+ and SPI Pump Module
(AccuMax & Hot Shot-II systems shown)

## Slide 22: SAI 85+ & SPI AERIALS, STREET SIDE PUMP CONTROL PANEL (AccuMax System Shown)

## Slide 23: SAI 85+/SPI CURB SIDE SUCTION INLETS & DISCHARGE OUTLETS
Removable Service/Inspection Panels Concealed Electric Gate Valves with Overrides

## Slide 24: SAI-75 AERIAL STREET SIDE PUMP CONTROL PANEL (AccuMax System Shown)
Street Side Control Panel Curb Side Outlets & Inlets

## Slide 25: INDUSTRIAL PUMP MODULES CONSTRUCTION METHODS & MATERIALS
304 STAINLESS STEEL CONSTRUCTION THROUGHOUT
BOLTED 12-GAUGE MODULE FABRICATIONS TIG WELDED WATER & FOAM MANIFOLDS

## Slide 26: BRAND-X SUCTION INTAKE MANIFOLD
Competitor’s High-Volume Intake Manifold, Square Corners:
POOR FLOW: the upper intakes have more water flowing through than the lower ones (red on top versus orange on bottom), thus the flow of the water in the manifold is disjointed and turbulent.

## Slide 27: INDUSTRIAL FIRE PUMP SUCTION WATERWAYS Computerized Photos of Sutphen Aerial (left) and Pumper (right) Suction Waterway depicts even volumetric flow at all intakes and laminar flow throughout the entire manifold, bottlenecked ONLY at the Pump Impeller Inlet.

## Slide 28: CONVERSION OF EXISTING INDUSTRIAL APPARATUS
ORIGINAL HOT SHOT (Driveline-Driven/Non-Servo Controlled Foam Pump)

## Slide 29: DISASSEMBLY/REMOVAL OF ORIGINAL HOT SHOT COMPONENTS

## Slide 30: FABRICATE AND INSTALL NEW WATER & FOAM MANIFOLDS

## Slide 31: CONVERTED FROM HOT SHOT DEMAND BALANCED PRESSURE TO FLOW BASED ACCUMAX

## Slide 32: CONVERSION OF RESERVE APPARATUS: TO A TOTE HAULER WITH OFF-LOAD SINGLE-POINT MANIFOLD

## Slide 33
For technical assistance with the promotion of or training on Industrial Apparatus Pump Systems, Jim Kirvida and Design Staff are personally available via email and phone calls; or, to accompany the Sutphen Sales Representative when visiting a Refinery, Terminal, or Oil Field.